## Slide 1: CIT-422 Computer Graphics and Image Processing Sessional
Rafid al Nahiyan
Id: 1702032
Reg: 7602
Pixel adjustment between hardware and software of a monitor

## Slide 2: Pixel adjustment
Monitors also perform hardware and software pixel adjustments to display images accurately and efficiently. These adjustments ensure that the input signal from the graphics processing unit (GPU) is rendered correctly on the monitor's screen, taking into account the monitor's physical characteristics, native resolution, color accuracy, and other display settings. Below are the main hardware and software pixel adjustments in monitors:

## Slide 3: Hardware pixel adjustment
  a. Native Resolution: Monitors have a fixed number of physical pixels that make up their native resolution. The hardware scaler adjusts the incoming pixel data to fit the native resolution without distortion. If the input resolution differs from the native resolution, the hardware scaler may upscale or downscale the image.
  b. Refresh Rate: The monitor's refresh rate determines how many times per second the screen is updated with new pixel data. The hardware ensures that the incoming pixel data is refreshed at the monitor's specified refresh rate to avoid artifacts like screen tearing.

## Slide 4: Hardware pixel adjustment (cont…)
c. Color Calibration: High-quality monitors often have hardware-based color calibration capabilities. The hardware is calibrated to match industry color standards (e.g., sRGB, Adobe RGB) to ensure accurate color representation and consistency.
d. Color Gamut and Depth: Color gamut refers to the range of colors that a device or system can reproduce or display. It is a three-dimensional representation of all the colors that can be created by combining different amounts of three primary colors: red, green, and blue (RGB). Monitors may have different color gamuts and bit depths. The hardware adjusts the pixel values to match the monitor's specific color capabilities.

## Slide 5: software pixel adjustment
a. Graphics Driver Settings: The graphics driver communicates with the monitor to configure display settings such as resolution, refresh rate, color profile, and gamma correction. The software ensures that the GPU outputs the correct pixel format compatible with the monitor.
b. Scaling: If the GPU output resolution differs from the monitor's native resolution, software scaling may be applied to adjust the pixel data to fit the monitor's resolution. This allows the display of content at various resolutions without distortion.

## Slide 6: software pixel adjustment(Cont…)
c. Color Profiles: The GPU may apply color profiles to adjust the color representation of the pixels to match the monitor's color gamut and calibrated settings. Color profiles ensure that colors appear consistent across different devices.
d. Image Enhancement: Some graphics drivers offer image enhancement features like sharpening, contrast enhancement, or color adjustments. These adjustments can be applied in software to improve image quality and visual appearance.

## Slide 7: software pixel adjustment(Cont…)
e. Frame Buffer: The GPU's frame buffer temporarily holds the pixel data before it is transmitted to the monitor. The frame buffer allows the GPU to perform processing and adjustment on the pixel data before displaying it on the screen.

## Slide 8: conclusion
It's important to note that some adjustments, like exposure settings (shutter speed, aperture), ISO sensitivity, and lens quality, mainly occur in hardware. However, many other adjustments, especially those related to color, noise, and image enhancement, are handled through software algorithms in the camera's processing pipeline.
The combination of hardware and software adjustments ensures that the final image produced by a digital camera is of high quality, accurately represents the scene, and meets the user's preferences.